## Slide 1: BLE Localiser
iOS Conf SG (19-20 Oct 2017)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/ble-localiser

## Slide 2: Demo
BLE Localisation
Manual Control

## Slide 3: The hardware
Raspberry Pi 3
  Wifi, Bluetooth (LE)
  Raspbian OS
Pimoroni Unicorn Hat
  8 x 8 RGB LEDs
  Python Library provided by manufacturer
iPad Mini 2 + Swift App
Supporting Gear
  Asus 4G-AC55U Wifi Router
  3x Tripod
  3x Xiaomi 10000mAh Power Bank

## Slide 4: Layout
2m
2m
2m

## Slide 5: System overview
Advertisement Packets
x LEDs + colour

## Slide 6: Workflow
n x RGB (255, 255, 255)
Unix Domain Socket
Receive signal strength of advertisement packets
Calculate and send LED information
via UDP
n x RGB (255, 255, 255)
Listening UDP Socket
Listening Unix Domain Socket
Unicorn Library

## Slide 7: Getting BLE RSSI on iOS?
Received Signal Strength Indicator
BLE Scan with Duplicate keys enabled
  centralManager.scanForPeripherals(withServices: nil, options: [CBCentralManagerScanOptionAllowDuplicatesKey : true])
Get Relative Signal Strength Indication (RSSI) in dBm
  CBCentralDelegate
  func centralManager(_ central: CBCentralManager, didDiscover peripheral: CBPeripheral, advertisementData: [String : Any], rssi: NSNumber)

## Slide 8: Distance(m) <-> RSSI formula
  Propagation Constant (Path Loss) in free space = 2
  dBm @ 1m: Reference Transmit Power at Source = -60.0 for RPi3
Referenced from https://stackoverflow.com/questions/20416218/understanding-ibeacon-distancing/20434019#20434019

## Slide 9: But RSSI values fluctuate widely…

## Slide 10: Do a Trimmed Mean
Trim outlier values from a set
Obtain values in a fixed queue
Sort the values
Remove the 20% outliers and average the rest -> 1.43m
Oldest |  |  |  |  |  |  |  |  | Newest
1.1 | 5.0 | 1.4 | 1.2 | 0.1 | 1.6 | 0.2 | 1.5 | 1.8 | 4.9
Smallest |  |  |  |  |  |  |  |  | Largest
0.1 | 0.2 | 1.1 | 1.2 | 1.4 | 1.5 | 1.6 | 1.8 | 4.9 | 5.0
Smallest |  |  |  |  |  |  |  |  | Largest
 |  | 1.1 | 1.2 | 1.4 | 1.5 | 1.6 | 1.8 |  | 

## Slide 11: Trilateration of 3 beacon distances
Determine the intersections of 3 spheres given the centres and radii
3 Sphere Simultaneous Equations:
Solve for x, y and z
https://en.wikipedia.org/wiki/Trilateration

## Slide 12: Check out the SP Booth to find out more

## Slide 13: Lets try averaging the last few values?
Implement a fixed queue
Average of values -> 1.8m
Oldest |  |  |  |  |  |  |  |  | Newest
1.1 | 5.0 | 1.4 | 1.2 | 0.1 | 1.6 | 0.2 | 1.5 | 1.8 | 4.9

## Slide 14: Compile Swift Apps on RPi
Raspbian now supported together with Ubuntu
Swift 3.1.1 with Swift Package Manager for Raspbian
  https://www.uraimo.com/2017/09/06/A-small-update-on-Swift-for-raspberry-pi-zero-1-2-3/
  sudo apt install libpython2.7 clang

## Slide 15: Cross compile ARM Swift apps on your Mac
Supports only up to Swift 3.0.2
Build the Swift Package Manager that supports Swift 3.0.2
  Checkout the 30 April 2017 commit:
  git clone https://github.com/apple/swift-package-manager.git
  git checkout 09a6bf19b4e31d9348d98efd9db09298da152315
Look out for libraries that require system header directory
  Eg. https://github.com/PureSwift/CSwiftBluetoothLinux
  /usr/include/…
  Go to Recovery mode to disable System Integrity Protection (SIP)