## Slide 1: BLE Localiser (Full)
iOS Dev Scout (5 Dec 2017)
iOS Conf SG (19-20 Oct 2017)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/ble-localiser

## Slide 2: iOSConfSG 2017

## Slide 3: Demo
BLE Localisation
  As distance ↓, LEDS ↑
Manual Control

## Slide 4: The hardware
Raspberry Pi 3
  Wifi, Bluetooth (LE)
  Raspbian OS
Pimoroni Unicorn Hat
  8 x 8 RGB LEDs
  Python Library provided by manufacturer
iPad Mini 2 + Swift App
Supporting Gear
  Asus 4G-AC55U Wifi Router
  3x Tripod
  3x Xiaomi 10000mAh Power Bank

## Slide 5: Layout
2m
2m
2m

## Slide 6: System overview
Advertisement Packets
x LEDs + colour

## Slide 7: Workflow
n x RGB (255, 255, 255)
Unix Domain Socket
Receive signal strength of advertisement packets
Calculate and send LED information
via UDP
n x RGB (255, 255, 255)
Listening UDP Socket
Listening Unix Domain Socket
Unicorn Library

## Slide 8: Initial OS Selection challenges
Unix Domain Socket
Listening UDP Socket
Listening Unix Domain Socket
Unicorn Library
Swift Compiler on RPi (Before Sept 2017)
  Only runs on Ubuntu
Unicorn library on RPi
  Only runs on Raspbian
 | Ubuntu | Raspbian
Swift Compiler | ✓ | X
Unicorn library | X | ✓

## Slide 9: Let’s think outside the box

## Slide 10: Cross compile ARM Swift apps on your Mac
Supports only up to Swift 3.0.2
Build the Swift Package Manager that supports Swift 3.0.2
  Checkout the 30 April 2017 commit:
  git clone https://github.com/apple/swift-package-manager.git
  git checkout 09a6bf19b4e31d9348d98efd9db09298da152315
Look out for libraries that require system header directory
  Eg. https://github.com/PureSwift/CSwiftBluetoothLinux
  /usr/include/…
  Go to Recovery mode to disable System Integrity Protection (SIP)

## Slide 11: Swift on RPi (today)
Raspbian now supported together with Ubuntu
Swift 3.1.1 with Swift Package Manager for Raspbian
  September 2017
  https://www.uraimo.com/2017/09/06/A-small-update-on-Swift-for-raspberry-pi-zero-1-2-3/
  sudo apt install libpython2.7 clang

## Slide 12: Quick Refresher on Bluetooth Low Energy (BLE)
Introduced in Bluetooth 4.0 specification (2010)
Also known as Bluetooth SMART
Traditional Bluetooth Classic
  Higher Speed applications: Audio, networking
  Needs MFI (Made for iPod/iPhone/iPad) certification
Target applications
  Wireless battery-powered sensors eg. heart rate, thermometer, fitness
  Location tracking and information serving eg. iBeacons

## Slide 13: Bluetooth Broadcasting on RPi
CoreBluetooth
Use external library https://github.com/PureSwift/BluetoothLinux

## Slide 14: Limitations on iOS CoreBluetooth
No official API to get Mac Address of advertising packet
Random UUID assigned to every new device
Cannot easily identify the RPis across multiple iOS devices

## Slide 15: To solve the identification problem
RPi embeds unique ID into Bluetooth device name
Linux commands to run
  hciconfig hci0 name “pib-xx”
  hciconfig hci0 down
  hciconfig hci0 up

## Slide 16: iOS App
Receive signal strength of advertisement packets
Calculate and send LED information
via UDP
n x RGB (255, 255, 255)

## Slide 17: Getting BLE RSSI on iOS?
Received Signal Strength Indicator
BLE Scan with Duplicate keys enabled
  centralManager.scanForPeripherals(withServices: nil, options: [CBCentralManagerScanOptionAllowDuplicatesKey : true])
Get Relative Signal Strength Indication (RSSI) in dBm
  CBCentralDelegate
  func centralManager(_ central: CBCentralManager, didDiscover peripheral: CBPeripheral, advertisementData: [String : Any], rssi: NSNumber)
Receive signal strength of advertisement packets

## Slide 18: Distance(m) <-> RSSI formula
  Propagation Constant (Path Loss) in free space = 2
  dBm @ 1m: Reference Transmit Power at Source = -60.0 for RPi3
Referenced from https://stackoverflow.com/questions/20416218/understanding-ibeacon-distancing/20434019#20434019

## Slide 19: But RSSI values fluctuate widely…

## Slide 20: Lets try averaging the last few values?
Implement a fixed queue
Average of values -> 1.8m
Oldest |  |  |  |  |  |  |  |  | Newest
1.1 | 5.0 | 1.4 | 1.2 | 0.1 | 1.6 | 0.2 | 1.5 | 1.8 | 4.9

## Slide 21: Do a Trimmed Mean
Trim outlier values from a set
Obtain values in a fixed queue
Sort the values
Remove the 20% outliers and average the rest -> 1.43m
Oldest |  |  |  |  |  |  |  |  | Newest
1.1 | 5.0 | 1.4 | 1.2 | 0.1 | 1.6 | 0.2 | 1.5 | 1.8 | 4.9
Smallest |  |  |  |  |  |  |  |  | Largest
0.1 | 0.2 | 1.1 | 1.2 | 1.4 | 1.5 | 1.6 | 1.8 | 4.9 | 5.0
Smallest |  |  |  |  |  |  |  |  | Largest
 |  | 1.1 | 1.2 | 1.4 | 1.5 | 1.6 | 1.8 |  | 

## Slide 22: Trilateration of 3 beacon distances
Determine the intersections of 3 spheres given the centres and radii
3 Sphere Simultaneous Equations:
Solve for x, y and z
https://en.wikipedia.org/wiki/Trilateration

## Slide 23: Drawing the UI
Using a master UIView
Circles diameter indicates distance to beacon
Positioning everything relative to center of UIView for ease of calculation

## Slide 24: iOS Coordinate vs Cartesian Coordinate
X-positive
Y-positive
X-positive
Y-positive

## Slide 25: Remap the Cartesian (meters) -> iOS Coordinate
Convert meters to pixels
  50 pixels / meter
Convert Cartesian -> iOS
  X: Add half-width to compensate origin on left
  Y: Add half-width, invert the axis

## Slide 26: Sending and Receiving UDP
Why UDP frames?
  Fire and forget packets
Use IBM BlueSocket library
  https://github.com/IBM-Swift/BlueSocket
  Works on iOS, MacOS, Linux
What iOS app sends
  number of LEDs + RGB colour values (255, 255, 255)
Calculate and send LED information
via UDP
n x RGB (255, 255, 255)
Listening UDP Socket

## Slide 27: Swift -> Python
App to app transfer
Network ports?
How about something more specialised?
Unix Domain Socket
Listening UDP Socket
Listening Unix Domain Socket

## Slide 28: What are Unix Domain Sockets?
A form of inter-process streaming communication
Properties
  Reliable
  Sequential
  Secure
Uses a file path eg. /home/user/socket.sock
Write/Receive bytes from the file path
File path can be secured by Unix permissions

## Slide 29: Unix domain socket send
Use IBM BlueSocket library again
  https://github.com/IBM-Swift/BlueSocket
Unix Domain Socket

## Slide 30: Unix domain socket receive (Python)
import socket
sock = socket.socket(socket.AF_UNIX, socket.SOCK_STREAM)
sock.bind(”socket.sock”)
sock.listen(1)
connection, client_address = sock.accept()
data = connection.recv(64)
Unix Domain Socket
Listening Unix Domain Socket

## Slide 31: Turn on required LEDS
Use Unicorn library to control LEDs
Iterate through all LEDs in row-major style
Turn on LED if (x * y) < (number to turn on)
Listening Unix Domain Socket
Unicorn Library

## Slide 32: RPi -> Unicorn Hat
Uses 5V Power, GND, PWM
Pulse Width Modulation (PWM)
  BCM18/PWM0
https://pinout.xyz/pinout/unicorn_hat
n x RGB (255, 255, 255)
Unicorn Library

## Slide 33: Final thoughts
Greater appreciation of localization technologies
Combined many tech concepts
  BLE, Swift on iOS, Swift on RPi, Python, UDP, Unix Sockets, Hardware
Finally given the talk I wanted to give at iOSConf!!!
iOS Dev Scout (5 Dec 2017)
iOS Conf SG (19-20 Oct 2017)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/ble-localiser